## Slide 1
VLM-Guided Robot Reaching
Language-conditioned tabletop manipulation with a vision-language model in the loop
A frozen Qwen3-VL detector feeds a behaviour-cloned navigation policy that drives a UR5e arm to touch a named object.
Onuralp Güvercin · Deep Learning in Robotics · Final Project

## Slide 2
Objective
WHAT ARE WE SOLVING?
▸ Task: a robot arm must reach out and touch a specific object named in natural language — e.g. "the red cube".
• Scene: a tabletop with 2–4 differently coloured boxes and spheres at random positions (6 colours × 2 shapes).
• The robot sees only a top-down camera image; it is never told the target's coordinates.
▸ The central question
• Can a vision-language model act as the "eyes" that localise the target, while a small learned policy acts as the "hands" that move toward it?
▸ Success metric
• An episode succeeds if the end-effector makes contact with — or comes within 5 cm of — the correct target.
• We report success rate, final EE-to-object distance, and steps taken.
VLM-Guided Robot Reaching
1

## Slide 3
System Architecture
PERCEPTION → CONTROL → ACTION, IN A CLOSED LOOP
MuJoCo Env
top-down image + ee_pos
Qwen3-VL (frozen)
image + object name → bbox (cx,cy,w,h)
NavigationMLP
[bbox, ee_pos] → H × Δee (metres)
UR5e Arm
apply H deltas → contact?
Closed loop: the policy executes H steps, then re-queries the VLM (H steps = 1 VLM call).
• Perception (VLM): localises the named object as a normalised bounding box. Used off-the-shelf, weights frozen.
• Control (MLP): 7-D input [bbox(4) + ee_pos(3)] → 3·H end-effector deltas in metres.
• The policy is trained purely by behaviour cloning on a scripted expert — no reinforcement learning, no VLM training.
VLM-Guided Robot Reaching
2

## Slide 4
Method · 1 — Data Collection
TEACHING WITH A SCRIPTED EXPERT
▸ An automated expert generates the demonstrations — no human teleop.
• Each scene spawns 2–4 objects via rejection sampling (≥ 10 cm apart, unique colours).
• For every object, a straight-line controller drives the end-effector toward it in small 4 cm steps.
▸ What is recorded at each step
• the top-down RGB image (128×128),
• the end-effector position ee_pos (xyz),
• the ground-truth bounding box, computed by projecting the object through the camera matrix.
▸ Only successful reaches are saved
• contact is detected from MuJoCo geom collisions between gripper and target;
• collection is parallelised across worker processes, each with its own seed.
VLM-Guided Robot Reaching
3

## Slide 5
Method · 2 — Policy & Behaviour Cloning
A SMALL RESIDUAL MLP THAT OUTPUTS MOTION
▸ NavigationMLP — a residual MLP (width 512, 4 residual blocks, SiLU + LayerNorm).
• Input (7-D): bbox(cx,cy,w,h) + normalised ee_pos(x,y,z).
• Output (3·H): end-effector deltas Δee in metres, H steps ahead.
▸ Trained by behaviour cloning (supervised regression)
• Target = the expert's actual step-to-step Δee; loss = MSE on the deltas.
• AdamW + warmup→cosine LR; the output head is zero-initialised so the policy starts from gentle, near-zero motions.
▸ Honest evaluation
• Stratified train/val/test split by colour+shape; samples from one trajectory never leak across splits.
• Test RMSE ≈ 0.0007 m — the policy reproduces expert deltas almost exactly.
VLM-Guided Robot Reaching
4

## Slide 6
Method · 3 — Critical Design Choices
THE DECISIONS THAT MAKE IT WORK
▸ Fixed bounding box per episode.
• The bbox is read once and held constant; the loop closes on ee_pos, not on a re-detected box. This makes behaviour robust to frame-to-frame VLM jitter.
▸ Delta actions with clamping (±5 cm/step).
• Predicting relative motion (not absolute targets) keeps every step bounded and stable — no large jumps.
▸ Configurable horizon H (1–5).
• H = how many steps run per VLM query. Small H = more re-planning (costly, accurate); large H = more open-loop drift between queries.
▸ Robust VLM parsing + fallback.
• Strips <think> reasoning, auto-detects 0–1000 / 0–128 / 0–1 coordinate scales, and falls back to a GT bbox if a call fails.
VLM-Guided Robot Reaching
5

## Slide 7
We Did Not Train the VLM
A SCOPE DECISION — AND THE PATH WE WOULD TAKE
▸ In this project Qwen3-VL-4B is used frozen, off-the-shelf, as the detector.
• Fine-tuning a 4-billion-parameter vision-language model needs multi-GPU memory and long training runs — compute we did not have.
• So our contribution is the end-to-end pipeline + the control policy, with the VLM as a plug-in perception module.
▸ If compute had been available
• We would fine-tune the VLM with GRPO (Group Relative Policy Optimization).
• Reward = how well the predicted bbox matches the target (IoU / centre error), or even downstream reaching success.
• This adapts the detector to our exact camera, lighting, and object set — directly attacking the VLM-vs-GT gap shown in the results.
VLM-Guided Robot Reaching
6

## Slide 8
PPO vs GRPO — The Idea
GRPO DROPS THE CRITIC AND USES A GROUP BASELINE
PPO trains an extra Value Model ("critic"); GRPO replaces it by sampling a group and normalising rewards. (DeepSeekMath, 2024)
▸ PPO (top)
• needs a separate Value Model to estimate the baseline (advantage via GAE).
• = a second large network to train and store.
▸ GRPO (bottom)
• samples a GROUP of G answers per prompt,
• scores each with the reward model,
• uses the group's mean/std as the baseline — no critic at all.
VLM-Guided Robot Reaching
7

## Slide 9
PPO vs GRPO — The Loss Functions
SAME CLIPPED OBJECTIVE, DIFFERENT ADVANTAGE
Shared importance ratio:
PPO
GRPO
• Advantage Â comes from a learned critic V (GAE).
• Extra value network → more memory & compute.
• KL penalty keeps the policy near the reference.
• Â = reward normalised within the group (no critic).
• Group mean is the baseline → lighter & simpler.
• Same clipped surrogate + KL to the reference.
VLM-Guided Robot Reaching
8

## Slide 10
Results · Success Rate
VLM-IN-THE-LOOP vs GROUND-TRUTH BBOX (ORACLE)
▸ Same policy in both runs.
• Only the bbox source changes.
▸ GT bbox peaks at H=2 → 100%.
▸ VLM bbox is flatter: 65–78%.
• The gap is the cost of imperfect perception.
▸ VLM degrades least at H=4–5,
• where open-loop drift hurts both runs anyway.
VLM-Guided Robot Reaching
9

## Slide 11
Results · Trends & A Real Episode
ACCURACY VS HORIZON, AND WHAT IT LOOKS LIKE
VLM-bbox episode (H=2): the predicted box (red) tracks the blue cube as the arm reaches it.
▸ Final distance
• GT reaches ~6 cm at best.
• VLM stays ~14–23 cm — bbox error biases the goal point.
▸ Sweet spot: H = 2–3
• enough look-ahead, not yet drifting open-loop.
▸ Takeaway
• the controller is near-perfect; perception is the limiter.
VLM-Guided Robot Reaching
10

## Slide 12
Results · What the Gap Means
READING THE NUMBERS
▸ The policy is essentially solved.
• Test RMSE ≈ 0.0007 m, and with oracle bboxes success reaches 100% (H=2). The MLP is not the bottleneck.
▸ Every VLM-run failure traces back to the bounding box.
• A box that is off-centre or wrong-sized shifts the goal the arm aims at — so the arm confidently reaches the wrong place.
• Because the bbox is fixed per episode, an early detection error persists for the whole reach.
▸ Horizon is a perception-cost trade-off.
• Small H re-queries the VLM often (accurate but slow); large H drifts open-loop. H=2–3 balances both.
▸ Implication: improving perception — not control — is what raises success. That is exactly what GRPO fine-tuning would target.
VLM-Guided Robot Reaching
11

## Slide 13
Conclusion & Future Work
WHAT WE LEARNED
▸ A frozen VLM + a tiny behaviour-cloned MLP is enough to build a working language-conditioned reaching system.
▸ The learned controller is near-perfect — up to 100% success with oracle bboxes; it is not the limiting factor.
▸ Perception is the bottleneck — swapping the oracle for the off-the-shelf VLM costs ~15–25 success points.
▸ Clear next step:
• fine-tune the VLM with GRPO (reward = bbox accuracy / reaching success) to close the perception gap — the one piece compute prevented here.
• GRPO is the natural fit: the reward is cheap to compute and it needs no value network.
▸ Practical operating point: horizon H = 2–3 — strong accuracy with fewer VLM queries.
VLM-Guided Robot Reaching
12